## Slide 1: Build Your Own Computer INFO 450

## Slide 2: Reasons to Build a PC
Computers are surprisingly easy to build.
* Money Saving
* Performance
* Satisfy Personal needs

## Slide 3: Parts Required:
Case
Power Supply
Motherboard
CPU
Memory
Video Card
Sound Card, Network Card, Modem…
Hard Drive(s)
DVD ROM/RW; Blue Ray
Keyboard, Mouse, Monitor

## Slide 4: Cases
Antec: Most popular
Lian-Li : Expensive, Top Rated
Thermaltake
Cooler Master
Nzst
Enlight
Corsair
Raidmax: low level popular case
Rosewill: Bang for the buck

## Slide 5: Case accessories: Fan, Cooling systems
Exhaust fans
Liquid cooling
Heat Sink

## Slide 6: Power Supply
Know what the power requirements are for the hardware you have installed or will install in your computer, check out these wattage requirements for the common computer parts

## Slide 7
Motherboard 15-30 watts
Low-end CPU 20-50 watts
Mid to high range CPU 40-150 watts
RAM 5 to 10 watts per Module
PCI add-in card 5 watts
Low to mid level graphics card 20-60 watts
High-End graphics card 100-250 watts
IDE hard drive 5-20 watts
Optical drives 10-25 watts

## Slide 8: You should add up your estimated requirements, add another 30% or so for safety and upgrades to get a rough idea of your minimum requirement. You should always go more than the minimum.
If you are into top of the line, heavy graphics, overclocking, bells and whistles, start with a 600 watt power supply at least.

## Slide 9: Motherboard
Intel Based
Desktop sockets Slot 1 • Socket 370 • Socket 423 • Socket 478 • LGA 775 • LGA 1156 • LGA 1366 • LGA 1155 • LGA 1356 • LGA 2011, LGA 2066
Mobile sockets Socket 441 • Socket 479 • Socket 495 • Socket M • Socket P • Socket G1 • Socket G2
Server sockets Socket 8 • Slot 2 • Socket 603 • Socket 604 • PAC418 • PAC611 • LGA 771 • LGA 1156 • LGA 1366 • LGA 1248 • LGA 1567 • LGA 1356 • LGA 2011
Legacy non-proprietary sockets Socket 1 • Socket 2 • Socket 3 • Socket 4 • Socket 5 • Socket 6 • Socket 7
http://en.wikipedia.org/wiki/LGA_771
http://en.wikipedia.org/wiki/LGA_775
http://en.wikipedia.org/wiki/LGA_1156
AMD based
AM4, TR4, AM3+, AM3, AM2+,AM2
CPU Sockets

## Slide 10: How to build a computer
Part 1: Choosing your parts
Part 2: The Build
Part 3: Installing OS